Monitoring Temperatures of
Central Heating Systems
with Raspberry Pi
programmed in Tcl
using SQLite3
and HTML5 for Browser Frontend
by Holger@Jakobs.com
2014-07-12

---
Raspberry Pi
- ARM-based Micro-
  computer
- Runs full-fledged
  Linux: e. g. Raspbian
- SD card slot for mass
  storage
- well connected:
  2 USB, HDMI + video output, RJ45 Ethernet
- GPIO port for all kinds of things

---
GPIO – general purpose I/O
- Two rows of pins at 2.54mm (1/10")
- Temperature Sensors need only 3 wires:
  - power + and −
  - data line

---
Temperature Sensor DS18B20

---
Temperature Sensor
Looks like a simple transistor
Does A/D conversion
Many sensors can be connected in parallel

---
Raspberry Pi in Housing

---
Drivers and Pseudo File System
- Raspbian comes with the necessary drivers:
  # modprobe w1-gpio
  # modprobe w1-therm
- Loading them creates a directory:
  /sys/devices/w1_bus_master1
- This directory will contain 1 directory per connected sensor:
  10-000802bf2c4b
  10-00080de3529a
- These contain among others a file:
  w1_slave

---
Reading from Pseudo Files
- Read the pseudo file w1_slave every 30s
  2e 00 4b 46 ff ff 09 10 ff : crc=ff YES
  2e 00 4b 46 ff ff 09 10 ff t=23187
- Reading can take up to 700 ms
- Temperature is in milli-centigrade
- Yeah – no conversion to metric is necessary!
- So it shows 23.187 °C – although the precision of three digits is nonsense
- regexp {t=([0-9]*)} [gets $f] – temperature
  set temperature [expr $temperature / 1000.0]

---
Architecture Overview
tempServer.tcl
tempHTTPserver.tcl
cron job
analysis of data
read pseudo
files
SQLite
save to db
tcp
call
acquire data
read db
SQLite
copy to
external server
read db

---
Software Architecture – 1st server
- tempServer.tcl
  - maintains arrays with min and max temperatures of all connected sensors
  - writes current, min and max temperatures to an SQLite3 db on the SD card (every 15 min)
  - is a tcp server which can list-sensors
    and get-temp
  - writes [array get sensorTemp] to the client
- Database file is copied to an external machine regularly via cron job.

---
Software Architecture – 2nd server
- tempHTTPserver.tcl
  - uses tempserver.tcl to get temperatures without the 700 ms delay
  - is a little Webserver for HTML, JavaScript, CSS and other files
  - URL
    /tempservice?getFromSensor&10-000802bf2c4b
    delivers temperature from named sensor
  - URL /tempservice?getFromAllSensors
    delivers a list of sensord ids and temperatures

---
Software Architecture – 2nd server
- tempHTTPserver.tcl (continued)
  - URL /getPageWithAllSensors
    constructs and delivers an HTML5 page including links to JavaScript files and canvases for all connected sensors.
- gauge.js provides the gauges which can be used like this: <div class='sensor'> … </div>
- updateGauges.js asks the server regularly for new values via AJAX calls.

---
Temperature Gauge

---
Plans for the Future
- Gauges with two indicators – one for supply (red) and one for return flow (blue)
- Collection of gauges from several Raspberry Pis in one big panel with tabs
- Convenient data export of recorded values for analysis with other software (spreadsheet)
- Monitoring of temperatures (min/max) with alarm messages (e-mails, text messages, Android notifications)
- Android app for smartphone and tablet

---
Questions? Suggestions?

---
THANK YOU